# HC-06 / STM32G4 Communication Protocol
Project: PSG5 Wireless Interface
Transport: Bluetooth Classic SPP (HC-06)
Physical Layer: UART (USART2, 8N1)

## 1. Overview
This protocol defines a lightweight, robust binary communication structure between:
- Android application (master)
- STM32G4 firmware (device)
- via HC-06 Bluetooth SPP module
The protocol is:
- Fixed-length frame
- Byte-stream tolerant
- Self-synchronizing
- Protected with CRC8
- Suitable for command/response architecture

## 2. Frame Structure
Each frame has the following structure:
Byte Index	Field	Size	Description
0	SYNC	1 byte	Fixed value 0xA5
1	CMD	1 byte	Command identifier (0x00–0xFF)
2–3	W1	2 bytes	Data word 1 (little-endian)
4–5	W2	2 bytes	Data word 2 (little-endian)
6–7	W3	2 bytes	Data word 3 (little-endian)
8	CRC	1 byte	CRC8 over bytes 1–7

Total frame size: 9 bytes

## 3. Byte Order
All 16-bit words are transmitted in little-endian format:
uint16 value = 0x1234
Wire format = 34 12

## 4. CRC Definition
CRC8:
- Polynomial: 0x07
- Initial value: 0x00
- Calculated over bytes:
[CMD][W1_L][W1_H][W2_L][W2_H][W3_L][W3_H]
SYNC byte (0xA5) is NOT included in CRC.
If CRC does not match:
- Frame is discarded
- Parser waits for next SYNC (0xA5)
This allows automatic resynchronization after byte loss or corruption.

## 5. Command Architecture
The protocol is command/response.
Response command is:
RESPONSE_CMD = CMD | 0x80
Examples:
Command	Response
0x01	0x81
0x02	0x82
0x03	0x83

## 6. Implemented Commands

### CMD 0x01 — Initialize PSG5 Communication
Purpose:
Calls InitPSG5Comm();
Request Frame
A5 01 00 00 00 00 00 00 CRC
Response
A5 81 00 00 00 00 00 00 CRC
Additionally, STM32 sends ASCII:
CMD01 InitPSG5Comm OK

### CMD 0x02 — Read DFI
Purpose:
Reads:
float dFi = ReadDfi();
The float is converted to signed 16-bit:
int16 = round(dFi * 256 / 3)
This preserves compatibility with existing ECU scaling.
Request
A5 02 00 00 00 00 00 00 CRC
Response
A5 82 00 00 00 00 [DFI_L][DFI_H] CRC
Where:
DFI_S16 = round(dFi * 256 / 3)
To convert back on Android:
float dFi = DFI_S16 * 3 / 256
Example:
If:
dFi = 1.5
Then:
DFI_S16 = 1.5 * 256 / 3 ≈ 128
Response W3:
80 00 (0x0080)

### CMD 0x03 — Write DFI
Purpose:
Writes a DFI value.
Android sends:
int16 scaled = round(dFi * 256 / 3)
STM32 converts:
float dFi = scaled * 3 / 256
WriteDfi(dFi);
Request Example
For dFi = 1.5:
Scaled = 128 = 0x0080
A5 03 00 00 00 00 80 00 CRC
Response
A5 83 00 00 00 00 00 00 CRC
ASCII message:
CMD03 WriteDfi OK

## 7. ASCII Debug Output
The STM32 also supports sending ASCII debug strings.
Example:
CMD02 ReadDfi s16=128
These messages are for development/debug only and are independent of binary frames.

## 8. Example Full Frame (Hex)
Example: Write DFI = 1.5
Payload before CRC:
03 00 00 00 00 80 00
Compute CRC8 over above bytes → example result: XX
Final frame:
A5 03 00 00 00 00 80 00 XX

## 9. Design Characteristics
- Fixed small frame (9 bytes)
- Self-resynchronizing
- CRC protected
- Deterministic timing
- Binary efficient
- Supports up to 256 commands
- Supports 3 parameters per command
- Fully endian-defined

## 10. Scaling Summary
Quantity	Formula
Encode float → int16	round(dFi * 256 / 3)
Decode int16 → float	scaled * 3 / 256

Range of int16:
-32768 to +32767

## 11. Transport Layer
- Bluetooth module: HC-06
- Mode: Classic SPP
- UART: 8N1
- Baud rate: configurable (default 9600 unless changed)